## Slide 1: GraphAttack+MAPLE: Optimizing Data Supply for Graph Applications on In-Order Multicore Architectures
Aninda Manocha, Marcelo Orenes-Vera, and Esin Tureci
November 18, 2021

## Slide 2: Graphs and Big Data
Machine learning and data science process large amounts of data
  Dense data (e.g. images) offer massive amounts of parallelism
Images from TripSavvy, Neo4j, and MIT Sloan Management Review
Graph databases and structures can efficiently represent big data
  E.g. social networks
Graph applications in big data analytics
  E.g. recommendation systems
How to efficiently compute with sparse data?

## Slide 3: Modern Technology Trends and Graph Applications
Modern system designs employ specialized hardware (e.g. GPUs and TPUs) for heterogeneous parallelism
  Significantly benefit compute-bound workloads
Image from Synopsys
We need efficient graph processing techniques that can scale!
Amdahl’s Law perspective: faster compute causes relative memory access time to increase
  Leads to memory latency bottlenecks
Many graph applications are memory-bound
Datasets are massive and growing exponentially
  The ability to process modern networks has not kept up

## Slide 4: Graph Applications: Access Patterns are Irregular
Iterative, frontier-based graph applications
  Describes many graph processing workloads (e.g. BFS, SSSP, PR)
0
3
2
1
4
Frontier nodes processed in parallel
0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
0
1
2
3
4
3
4
1
0
2
frontier
node_vals
0
1
2
1
2
0
1
4
3
2
0
1
4
3
2
Stores IDs of nodes to process
Stores node property data
for node in frontier:
val = process_node(node)
for neib in G.neighbors(node):
update = update_neib(node_vals,val,neib)
if(add_to_frontier(update)):
new_frontier.push(neib)
0
Indirect memory access due to neighbor locations
1
3
2
4
Updates are irregular!
(hops from 0)
neighbors
nodes
Iterative, frontier-based graph application
Indirect accesses to neighbor data
  Conditionally populate next frontier

## Slide 5: Neighbor Memory Accesses: The Problem
Irregular accesses experience cache misses
CPU
L1 Cache
Last-Level Cache (LLC)
Main Memory
200 cycle latency
34 cycle latency
4 cycle latency
On-chip
Runtimes measured on a simulated in-order core.
Note: these latencies are an example for a Haswell-like core.
Neighbor Memory Accesses (NMAs): irregular memory accesses in critical path

## Slide 6: Inefficiencies of Out-of-Order (OoO) Cores
Power-hungry structures for OoO scheduling
Adds significant area and power overhead compared to in-order cores
NMAs challenge latency tolerance achieved through instruction-level parallelism (ILP)
Dependencies lead to stalling and inhibit ILP
NMAs have long latencies
Prior works augment already complex core designs with additional hardware
e.g. prefetchers [1, 2] and in-memory technologies [3]
1
2
3
4
5
Insts
time
In-Order Core Execution
time
Out-of-Order Core Execution
execution
memory access
1
2
3
4
5
Insts
time
In-Order Core Execution
time
Out-of-Order Core Execution
Memory access dependencies
1. Ainsworth and Jones. ASPLOS ‘18. 2. Basak et al. HPCA ‘19. 3.Ahn et al. ISCA ‘15.

## Slide 7: Prior Work on Graph Processing
Prefetching
  Programmable, event-triggered [Ainsworth ASPLOS ‘18]
  DROPLET [Basak HPCA ‘19]
Accelerator-oriented approaches
  Tesseract [Ahn ISCA ‘15]
  Graphicionado [Ham MICRO ‘16]
Customized memory subsystems
  OMEGA [Addisie IISWC ‘18]
  PHI [Mukkara MICRO ‘19]
Variable processing per vertex lowers prefetch accuracy, incurs additional energy cost
Application restrictions (e.g. vertex programming model), not general-purpose
Invasive modifications/ specializations in the memory hierarchy
Notes: Prior work has extensively explored improving graph processing from both ends of the computing stack.
Software-based techniques in general provide frameworks that aim to be scalable, parallel solutions on shared memory systems. These works use thread-level-parallelism to address memory latency bottlenecks. By having multiple threads issue irregular memory accesses simultaneously, these techniques can exploit Memory Level Parallelism (MLP). Additionally, these techniques often involve complex scheduling routines and dynamic adjustments based on runtime characteristics. While these approaches are effective for performance improvements, they are limited by the underlying hardware, for example the number of threads or cores available. Thus, we need a flexible hardware solution that synergizes with the efforts of these approaches, such as a flexible backend target that exposes the long-latency memory access bottlenecks.
Meanwhile, hardware-based approaches have incorporated a number of different specializations. One avenue has been data-structure aware prefetching, where regular memory accesses guide irregular access prefetches. The system is specialized to know which data structures are regularly and irregularly accessed, and can perform the prefetching accordingly. Other approaches have been accelerator-oriented, creating specialized graph analytics accelerators that strive for energy efficiency. These approaches have involved specialized pipelines, such as separate modules for node and edge processing, processing near-memory, and on-chip scratchpads. Lastly, other prior work has focused on memory subsystem customizations, including reserving caches for nodes that are expected to be accessed the most frequently. All of these hardware-oriented approaches impose significant application restrictions, such as requiring the vertex programming model, or require invasive architectural modifications. We need a less specialized, more general-purpose solution that is adaptable and easy to incorporate into modern heterogeneous, parallel systems.

## Slide 8: Prior Work on Graph Processing
Software-oriented techniques:
  Aim for scalable parallel solutions
    Thread-level-parallelism to exploit MLP
    Complex scheduling routines
    Dynamic adjustments based on runtime characteristics
Well-known frameworks
  GraphMat [Sundaram PVLDB ’15]
  Gunrock [Wang PPoPP ’16]
  GraphIt [Zhang PACMPL ‘18]
Limited by the hardware resources, need flexible backend target
Software-based approaches focus on algorithmic improvements rather than targeting the LLAMAs with hardware innovations
Notes: Prior work has extensively explored improving graph processing from both ends of the computing stack.
Software-based techniques in general provide frameworks that aim to be scalable, parallel solutions on shared memory systems. These works use thread-level-parallelism to address memory latency bottlenecks. By having multiple threads issue irregular memory accesses simultaneously, these techniques can exploit Memory Level Parallelism (MLP). Additionally, these techniques often involve complex scheduling routines and dynamic adjustments based on runtime characteristics. While these approaches are effective for performance improvements, they are limited by the underlying hardware, for example the number of threads or cores available. Thus, we need a flexible hardware solution that synergizes with the efforts of these approaches, such as a flexible backend target that exposes the long-latency memory access bottlenecks.
Meanwhile, hardware-based approaches have incorporated a number of different specializations. One avenue has been data-structure aware prefetching, where regular memory accesses guide irregular access prefetches. The system is specialized to know which data structures are regularly and irregularly accessed, and can perform the prefetching accordingly. Other approaches have been accelerator-oriented, creating specialized graph analytics accelerators that strive for energy efficiency. These approaches have involved specialized pipelines, such as separate modules for node and edge processing, processing near-memory, and on-chip scratchpads. Lastly, other prior work has focused on memory subsystem customizations, including reserving caches for nodes that are expected to be accessed the most frequently. All of these hardware-oriented approaches impose significant application restrictions, such as requiring the vertex programming model, or require invasive architectural modifications. We need a less specialized, more general-purpose solution that is adaptable and easy to incorporate into modern heterogeneous, parallel systems.

## Slide 9: Our Approach: GraphAttack+MAPLE
A hardware-software co-design to tolerate latency in graph applications
  Compiler performs dependence graph analysis to reveal efficient Producer/Consumer program slicing
    Overlaps the long latencies of NMAs
  Multicore architecture features specialized HW unit, MAPLE
    Issues and tracks multiple NMAs
C0
C1
2 Parallel In-Order Cores
Memory
P
C
GraphAttack: 1 Producer/Consumer Pair of 2 In-Order Cores
Memory
Offers significant performance improvements
  Up to 4.68x speedup over traditional parallelism (InO cores)
  Up to 38.67x improvement in energy efficiency over OoO

## Slide 10: Outline
Motivation
Compiler Approach
GraphAttack Architecture
Evaluation
Conclusions

## Slide 11: Decoupling for Latency Tolerance
Data
Decoupling: static division of a program into a [data] Producer/Consumer pair
  Cores run independently; heterogeneous parallelism
Ideal: the Producer has no dependencies, so the Consumer never stalls after warm-up period!
Req
C
C
C
C
C
C
P
P
P
P
P
P
Warm-up period
C
C
C
C
C
C
C
C
C
C
Consumer
Memory Hierarchy
(value computation)
The Producer runs ahead and retrieves data for the Consumer
Producer
Homogeneous parallelism accelerates computation
Heterogeneous parallelism tolerates latency
(memory access, address computation)
Ideally, the Producer runs ahead of the Consumer
  Issues memory requests early and enqueues data
The Consumer consumes enqueued data and handles complex value computation
  Data has already been retrieved by the Producer
C
C

## Slide 12: Decoupling for Asynchronous Accesses
P
C
P
C
C
C
C
C
P
P
P
P
Next mem req asynchronously issued
Memory Level Parallelism
Waits for prev req to return with data
Asynchronous access data not later used on the Producer; allows Producer runahead
The Producer issues several non-asynchronous loads
The Producer issues several asynchronous loads
P
C
P
C
C
C
P
P
Decoupling into two instruction streams removes dependencies on each slice
  The Producer might have to stall waiting for long-latency loads, but doesn’t use data
  Usually, only the Consumer needs the data
Asynchronous accesses: accesses whose data is not later used on the Producer
  The Producer does not occupy pipeline resources waiting for their requests
  These loads asynchronously complete early and are maintained in specialized HW
  Asynchronous loads help maintain longer Producer runahead and exploit MLP
No asynchronous accesses; stalling due to long memory latency
mem access dependence

## Slide 13: Making NMAs Asynchronous Through Dependence Graph Analysis
Slice graph applications along their NMAs to create asynchronous accesses
  Producer handles all instructions necessary to determine address of NMA and issues access
  Consumer handles all instructions that depend on data returned from NMA
Dependence graph analysis can identify NMAs as pointer indirect accesses in innermost loop
  Competitive parallel implementations use RMWs, so NMAs can be loads or RMWs
  Search for accesses with addresses originating from earlier load
for node in frontier:
val = process_node(node)
for neib in G.neighbors(node):
update = update_neib(node_vals,val,neib)
if(add_to_frontier(update)):
new_frontier.push(neib)
Iterative, frontier-based graph application
Original Producer Consumer
Dependence graph analysis for Producer/Consumer slicing
The Producer issues the NMA, but does not have to wait for its return!

## Slide 14: Slicing with Dependence Graph Analysis
Identify Producer instructions
  Backward slice starting from NMA(s)
Identify Consumer instructions
  1) Forward slice starting from NMA(s)
  2) Backward slice from operations found in (1)
Handle duplicate instructions
  Leave duplicate arithmetic
  For loads and RMWs, Producer issues memory request and sends data to Consumer
Original
Producer
Consumer

## Slide 15: Compilation Procedure
1
Find NMAs
Identify pointer indirect accesses in innermost kernel loop
Search for loads and RMWs where address originates from earlier load
2
Slice Program:
Create Producer/Consumer slices based on NMA locations
Producer issues NMAs, Consumer uses their data
3
Check Memory Safety:
Ensure Producer, Consumer, and MAPLE do not have conflicts
Writes performed in disjoint memory regions
Error: Cannot identify NMA!
Error: Dependence graph is cyclic!
Warning: Producer and Consumer write to same region!

## Slide 16: Outline
Motivation
Compiler Approach
GraphAttack Architecture
Evaluation
Conclusions

## Slide 17: Layers Involved in each Technique
DAE [Smith ISCA ‘82], Pipette [Nguyen MICRO’20]
μarch changes visible with new ISA inst.
Programmable Prefetching [Ainsworth ASPLOS’18]
DeSC [Ham MICRO’15]
Compiler targeting new ISA inst.
Prior Work
Application
OS, Compiler, DSL (Domain Specific Language) backend
Architecture (ISA)
Processor Core Microarchitecture
RTL (e.g. Verilog)
DROPLET [Basak HPCA ‘19], IMP [Yu MICRO’15]
Use predictors to trigger prefetches
Slipstream [Sundaramoorthy ASPLOS ’00
Use predictors to orchestrate streams
Notes: To show where our work fits on the software-hardware stack, let’s revisit first the related work.
In this figure I show the layers of the stack involved in the hardware approaches we showed in the table before!
Hardware prefetching of Indirect memory accesses and Slipstream are only at the microarchitecture level, limiting the benefits to things that are known or predicted at runtime
while more holistic apporaches are architecturally exposed thru new instructions.
Programmable prefetching and DeSC also include a compiler pass to target these newly added ISA instructions.

## Slide 18: Layers Involved in each Technique
DAE [Smith ISCA ‘82], Pipette [Nguyen MICRO’20]
μarch changes visible with new ISA inst.
Programmable Prefetching [Ainsworth ASPLOS’18]
DeSC [Ham MICRO’15]
Compiler targeting new ISA inst.
Prior Work
Software Prefetching for IMAs [Ainsworth CGO’18]
Clairvoyance [Tran CGO’17]
Compiler-only approach
Application
OS, Compiler, DSL (Domain Specific Language) backend
Architecture (ISA)
Processor Core Microarchitecture
RTL (e.g. Verilog)
DROPLET [Basak HPCA ‘19], IMP [Yu MICRO’15]
Use predictors to trigger prefetches
Slipstream [Sundaramoorthy ASPLOS ’00
Use predictors to orchestrate streams
Notes: And Finally, software only-approaches optimize code at the compiler level, without New hardware involved.
While these approaches can provide good performance improvements, they are limited by the underlying hardware.
For example, In the case of Clairvoyance, the approach is only performing well, when used in conjunction with OoO cores with large instruction windows.

## Slide 19: Layers Involved in each Technique
DAE [Smith ISCA ‘82], Pipette [Nguyen MICRO’20]
μarch changes visible with new ISA inst.
Programmable Prefetching [Ainsworth ASPLOS’18]
DeSC [Ham MICRO’15]
Compiler targeting new ISA inst.
Provides an API that is targeted by automated compiler techniques
Our hardware approach doesn’t modify the core
API operations use existing memory instructions, so it is ISA-agnostic
Prior Work
GraphAttack
Software Prefetching for IMAs [Ainsworth CGO’18]
Clairvoyance [Tran CGO’17]
Compiler-only approach
Out-of core HW:
MAPLE
Application
OS, Compiler, DSL (Domain Specific Language) backend
Architecture (ISA)
Processor Core Microarchitecture
RTL (e.g. Verilog)
DROPLET [Basak HPCA ‘19], IMP [Yu MICRO’15]
Use predictors to trigger prefetches
Slipstream [Sundaramoorthy ASPLOS ’00
Use predictors to orchestrate streams
Notes: Now adding GraphAttack into the chart.
GraphAttack leverages the compiler layer to target our specialized hardware (MAPLE), thru its programming API.
The API operations use existing memory instructions, and so it is ISA-agnostic.
And our hardware approach does not modify the core, as it is connected to the Network on chip, as any other component of the SoC

## Slide 20: Hardware Support: MAPLE
In-order Producer and Consumer cores
MAPLE can issue and track multiple outstanding requests for Loads and RMWs
Asychronous RMWs require atomicity with memory requests
  Memory system guarantees exclusive permissions to data’s cache line
  Loaded data enqueued for Consumer, atomic store sent to memory
Notes: MAPLEs offers a software interface to its hardware specialization.
Its communication mechanism allows using MAPLE for, out-of-the-core, decoupling by offloading memory request to this shared device.
its programming model is easily extensible to incorporate other access patterns or more memory operations.
By using MAPLEs we can achieve software programmability, with the performance benefits often reserved to microarchitectural approaches, since
The decoupling and operations use existing memory instructions, load and stores, into a virtual page mapped to MAPLE hardware within the IO address range.
Since there are No new instructions and MAPLE is connected to the Network-on-Chip,, the Core remains unmodified.
And so it easy-to-adopt even in the context of an SoC generator framework, meaning that MAPLE can be included in a tapeout without affecting any of the other pieces of the SoC.
As shown in the picture, even Heterogeneous cores in the SoC could communicate with MAPLE.

## Slide 21: GraphAttack Hardware Support
Produce path (steps 1-6)
Consume path (steps A-B)
Producer/Consumer are ”roles” taken by software threads rather than a core-type (as in prior art)
Notes: This Figure shows the software-hardware timeline of Produce and Consume operations.
The are different types of Produce, a core can Produce data directly, or a pointer as we just saw,, and here we are explaining the pointer case, which involve MAPLE loading it from memory.
The produce path works as follows:
(1) It starts doing a store instruction of the pointer to fetch,, targeted to the base address of MAPLE instance’s logically ORed with the queue id, and operation code.
(2) The decoder at MAPLE identifies the operation as a pointer produce, and routes it to the store pipeline where it will reserve an entry in the corresponding queue;
(3) The pointer is first translated into a physical address thru the MMU, which is then requested to DRAM, using as transaction id, the index of the allocated entry in the queue;
(4) The initial store instruction is acknowledged back to the Access thread which considers the produce finished;
(5) The memory request reaches DRAM which responds to MAPLE;
(6) The response is decoded and stored in the corresponding queue entry
The consume path works as follows:
(A) Execute thread generates consume operation, which is implemented in the API as load to MAPLE. Once there, it is decoded and routed to the load pipeline;
(B) If the queue specified on the request is not empty, it would pop the head of the queue and return it as a response to the load instruction;
(C) The response reaches the core that is playing the Execute role, and the consume operation is finished.
This is the process for decoupling, and now I'm going to explain about how MAPLE can also be used for prefetching!

## Slide 22: MAPLE design
Load Pipeline: Consume data
Configuration Pipe: manage queues, bind Access/Execute threads, config LIMA, MMU, debug
Store Pipe: Push data and pointers (to fetch)
Notes: Here we can observe the breakdown of MAPLE into the 3 pipelines in yellow, and the queue controller, MMU.
The Configuration-pipeline is used to manage the queues and their binding to software threads, aside from configuring the MMU.
Queues are configured at runtime as they are implemented as circular FIFOs using the device scratchpad.
Depending on the program needs, it can have fewer but bigger queues, or many but smaller.
At the end of all 3 pipes, there is a final stage, to send a response back to the issuing core.
The Load-pipe (above) is solely used to consume data from the queues
And The Store-pipe (below) is used to receive data or pointers, as we have shown before
This design can receive pointers and send memory requests every cycle

## Slide 23
MAPLE can be instanced many times, e.g. in a tiled architecture. Each unit is addressed as a separate memory-mapped page (protected access).
The API implementation hides the management of physical MAPLE units to the software interface, which has an abstract concept of queues
Virtual memory for transparent usage of MAPLE
Processor Tiles
MAPLE Tiles
Accelerator Tiles
Images credit: DECADES Team
Each MAPLE unit contains a MMU with Translation Lookaside Buffer (TLB) and a Page Table Walker (PTW)
Notes: We have mentioned that our MAPLE API operations are under-the-hood loads and stores,
and so Cores interact with MAPLE by mapping it, into virtual memory.
Using virtual memory provides a Process, exclusive access to MAPLE hardware resources.
---A process with many threads can also map several MAPLE units, across the SoC, for example in a Tiled architecture.
The API, handles the mapping-process of MAPLE units internally, providing an abstract concept of software queues

## Slide 24: Outline
Motivation
Compiler Approach
GraphAttack! Architecture
Evaluation
Conclusions

## Slide 25: Graph/Sparse Applications
Vertex-programmable (VP) graph processing primitives:
  Breadth-First Search (BFS): Determine the distance (number of node hops) to all nodes.
  Single-Source Shortest Paths (SSSP): Determine the shortest distance (sum of path edge weights) to all nodes.
  PageRank (PR): Determine node ranks based on the distributed ranks of neighbors.
Sparse-Dense Hadamard Product (SDHP): Multiplication between a sparse and a dense matrix.
Bipartite Graph Projections (GP): Relate nodes in one partition based on common neighbors in the other.
Images from Wikipedia
Used in recommendation systems and sparse neural networks
Push- and pull-based graph processing primitives

## Slide 26: Methodology
4 input datasets per application
Clang/LLVM compiler
  Performs passes on C source code
MosaicSim1 cycle-driven simulator
  Models static and dynamic (control flow and memory aliasing) dependencies, and hardware resource use
Core models
  Simple, single-issue in-order processor
  Out-of-order processor with ideal control flow and memory speculation
Synthetic and real power-law inputs
Memory hierarchy and queue models
Core model parameter comparison
1 O. Matthews, A. Manocha, D. Giri, M. Orenes Vera, E. Tureci, T. Sorensen, T. J. Ham, J. L. Aragón, L. Carloni, and M. Martonosi. “MosaicSim: A Lightweight, Modular Simulator for Heterogeneous Systems,” In ISPASS, 2020.
Notes: ???

## Slide 27: GraphAttack Tolerates Latency and Better Utilizes Core Area
InO
InO
2 Out-of-Order Cores
P
C
8 In-Order GraphAttack Pairs
vs.
6.16x
InO
InO
InO
InO
InO
InO
InO
InO
InO
InO
InO
InO
InO
InO
P
P
P
P
P
P
P
C
C
C
C
C
C
C
vs.
OoO
OoO
16 Parallel In-Order Cores

## Slide 28: GraphAttack is Scalable and Energy-Efficient
vs.
2 In-Order Cores
1 GraphAttack Pair
InO
InO
P
C
7.18x
31.56x

## Slide 29: Hardware Integration with OpenPiton
For the evaluation of GraphAttack!, we integrated MAPLE into the open-source OpenPiton [Balkind ASPLOS’16] manycore, on its own tile.
The processor core (unmodified) can write and read from MAPLE using the Network-on-Chip (NoC)
Notes: For the evaluation of GraphAttack, and as part of the SoC design, we integrated MAPLE into the OpenPiton manycore, on its own tile.
We tested using off-the-shelf Ariane cores, that were developed by ETH Zurich
The processor core, which remains unmodified, can write and read from MAPLE using the Network-on-Chip (NoC)
The figure in the bottom represents a communication path from Ariane to MAPLE and back

## Slide 30: Evaluating MAPLE full-system on FPGA
Experimental setup: SoC prototype on FPGA VC707 composed of 2 Ariane Core and 1 MAPLE Tile. We evaluate applications full-stack on top of Linux v5.6-rc4
Notes: For the evaluation of MAPLE, we are using an FPGA chip prototype of 2 Ariane cores and 1 MAPLE Tile.
And we run applications at full-system, on top of LINUX.
NEXT
-----------
The evaluated system builds on top of the OpenPiton + Ariane framework with an RTL implementation of MAPLE integrated.
Since the main objective of OpenDCP is to provide MLP using simple cores in area-constrained systems, the overhead added by any memory tolerance mechanism must be minimal. Synthesis results show that the area of MAPLE is 0.019mm2, while a core tile has an area of 0.240mm. A single MAPLE device can provide MLP via communication queues for up to 8 pairs of decoupling threads, with an area overhead of just 0.49%

## Slide 31: Evaluating MAPLE full-system on FPGA
Notes: As I mentioned we generating the bitstream into FPGA of a prototype of 2 Ariane cores and 1 MAPLE unit, for demonstration.
And in the bottom some more details of the evaluation setup, like the caches used in Openpiton and their latency

## Slide 32: Demo running SDHP on top of Linux on FPGA
Notes: (click)
Now I LL show an actual DEMO run on FPGA of SDHP, using decoupling and prefetching through MAPLE.
The demo starts by booting Linux on the FPGA, and later we will run 4 programs to make performance comparisons:
We run the Original program and prefetching version using a single thread. AND then do-all parallelism and the decoupled version using 2 threads.
….Now it is finishing the Linux boot….
And these are the programs we are going to Run…....Jumping into the results
First single-thread baseline… then the prefetching version
------The output is the cycle count of the programs.
Then the 2-threads with traditional parallelism…. And then the decoupled version,

## Slide 33: Demo running SDHP on top of Linux on FPGA
2.2x
1 Access and 1 Execute thread Decoupling using MAPLE
VS 2-thread do-all parallelism
Notes: We can observe the cycle count from the DEMO in detail, and see that MAPLE decoupling provides 2.2x speedup over two-thread doall parallelism.

## Slide 34: Decoupling Performance Analysis on FPGA
MAPLE assistance for decoupling provides 3x speedup over pure software (SW-DAE)
MAPLE outperforms traditional parallelism across the board, achieving a geomean speedup of 1.8x over do-all (for 2 threads).
The FPGA emulation confirms our earlier simulation results!
3x
2.83x
1.8x
Notes: This graph shows the result we have just seen, and other 3 workloads using decoupling with MAPLE!
Here we compare the same decoupled program, using MAPLE-API for decoupling and a shared-memory implementation, normalized to the performance
of traditional parallelism (doall)
---For SPMV and BFS, pure software DAE is not effective, due to heavy load stalling in the Access thread, which prevents it from running ahead of the execute thread.
This is overcome by MAPLE, which provides hardware memory parallelism, and achieves 3x geomean speedup over shared-memory decoupling.
MAPLE also outperforms doall parallelism across the board, achieving a geomean speedup of 1.8x

## Slide 35: Area analysis of MAPLE’s RTL
MAPLE area = 180 um x 180 um
MAPLE RTL has been synthesized on 12nm at 1Ghz, and its area is 10% of that of an Ariane1 In-Order core tile (very area-efficient already)
Since each MAPLE can be supply data to 8 cores, this overhead means 1.2% per core tile
1. RISC-V Ariane CVA6. https://github.com/openhwgroup/cva6.
Notes: Regarding Area, MAPLE RTL has been synthesized on 12nm at 1Ghz and its area is 10% of that of an Ariane core tile (which very area-efficient in-order core already)
Since each MAPLE can supply of data to 8 cores, this overhead means just 1.2% per core tile

## Slide 36: MAPLE’s RTL Design & Verification
The RTL development process, was assisted since the beginning by RTL Formal Verification: (1) to make sure the design specification didn’t contain deadlocks, and (2) to verify that the RTL implementation was correct w.r.t the specification
We deliver an implemented and verified hardware unit that assist GraphAttack software innovations
Internal interactions
Core-MAPLE communication
Notes: The RTL development process was assisted since the beginning, by RTL Formal Verification:
First, to make sure the design specification itself didn’t contain deadlocks,
And Second, to verify that the RTL implementation was correct
We deliver an implemented and verified hardware unit that assist GraphAttack software innovations, conforming our hardware-software co-design

## Slide 37: Outline
Motivation
Compiler Approach
GraphAttack! Architecture
Evaluation
Conclusions

## Slide 38: Conclusions
Graph applications are bottlenecked by pointer indirect memory accesses for neighbor traversals, i.e. NMAs
GraphAttack: hardware-software co-design to efficiently target NMAs
  Producer/Consumer program slicing overlaps long memory latencies
    Flexibly supports graph applications from state-of-the-art benchmark suites
MAPLE issues and tracks multiple outstanding requests. Its specialized hardware does not need architecture or core changes. Unlike many prior art, it is easy to adopt.
  Simulation results demonstrate 2.48x speedup over parallel InO and 22.52x improvement in energy efficiency over OoO
  Full-stack SoC prototype evaluation shows geomean speedups of 2.27× and 2.35x over software decoupling and prefetching, respectively

## Slide 39: For More Information
Thank you to our collaborators:
Tyler Sorensen, Luwa Matthews, Jonathan Balkind, Fei Gao, Juan Luis Aragón, David Wentzlaff, Margaret Martonosi, and the rest of the DECADES team
Contact:
amanocha@princeton.edu
https://mrmgroup.cs.princeton.edu/
https://decades.cs.princeton.edu/
Open Source Tools:
https://github.com/amanocha/FAST-LLAMAs
https://github.com/PrincetonUniversity/DecadesCompiler
https://github.com/PrincetonUniversity/MosaicSim
morenes@princeton.edu
etureci@princeton.edu
Demos
Decoupling with Asymmetric Access/Execute threads https://youtu.be/elkQcMFSvoo
Decoupling and prefetching on top of Linux
https://youtu.be/YRbsjqzlTOM
Notes: And now I'm ready to take questions from the committee or the broader

## Slide 40: Backup Slides

## Slide 41: GraphAttack Hardware Support
In-order Producer and Consumer cores
MAPLE can issue and track multiple outstanding requests for loads and RMWs
ALU on MAPLE or Last-Level-Cache
  Performs “modify” operations
Asychronous RMWs require atomicity with memory requests
  Memory system guarantees exclusive permissions to data’s cache line
  Loaded data enqueued for Consumer, atomic store sent to memory
Blue arrows indicate datapath additions for terminal RMWs.
The numbers illustrate the order in which data proceeds through the system.
In-Order Core
L3 Cache
In-Order Core
Comm. Queue
Async. Access
at MAPLE
Producer
Consumer
L1 Cache
ALU
L1 Cache
Main Memory
1
2
3
4
7
6
5
8
L2 Cache
L2 Cache

## Slide 42: LIMA Unit
For LIMA operations:
Once the base address of arrays A and B are configured, it fetches the array B in chunks, which are then accessed in a streaming way, to later iterate word by word, and calculate the index to array A.
Notes: For LIMA operations:
Once the base address of arrays A and B are configured, it fetches the array B in chunks, which are then accessed word by word to calculate the index to array A.

## Slide 43: Graph Applications are Emerging Workloads
Big data naturally in the form of graphs
  Social networks
  Communication networks
  Biological networks
Graph/sparse computation kernels are widely used
  Recommendation systems
  Natural language processing
  Search engines (e.g. Google, Facebook)
  Community/cluster detection
Images from MIT Sloan Management Review, https://www.smartcitiesworld.net, and the European Bioinformatics Institute.
Notes: We currently live in an era where we need efficient processing of big data and much of this big data is naturally represented as graphs. Some examples are social networks, communication networks, and biological networks. In fact, Google uses a Knowledge Graph to store data and enhance its search results with information gathered from a variety of sources.
Therefore, graph and other sparse computation kernels are at the heart of many data analytic applications, such as recommendation systems, natural language processing, community/cluster detection, and of course search engines like Google and Facebook.

## Slide 44: Prior Work on Graph Processing
Prefetching
  Programmable, event-triggered [Ainsworth ASPLOS ‘18]
  DROPLET [Basak HPCA ‘19]
Accelerator-oriented approaches
  Energy Efficient Architecture [Ozdal ISCA ‘16]
  Graphicionado [Ham MICRO ‘16]
Customized memory subsystems
  OMEGA [Addisie IISWC ‘18]
  PHI [Mukkara MICRO ‘19]
Variable processing per vertex lowers prefetch accuracy, incurs additional energy cost
Application restrictions (e.g. vertex programming model), not general-purpose
Invasive modifications/ specializations in the memory hierarchy
Notes: Prior work has extensively explored improving graph processing from both ends of the computing stack.
Software-based techniques in general provide frameworks that aim to be scalable, parallel solutions on shared memory systems. These works use thread-level-parallelism to address memory latency bottlenecks. By having multiple threads issue irregular memory accesses simultaneously, these techniques can exploit Memory Level Parallelism (MLP). Additionally, these techniques often involve complex scheduling routines and dynamic adjustments based on runtime characteristics. While these approaches are effective for performance improvements, they are limited by the underlying hardware, for example the number of threads or cores available. Thus, we need a flexible hardware solution that synergizes with the efforts of these approaches, such as a flexible backend target that exposes the long-latency memory access bottlenecks.
Meanwhile, hardware-based approaches have incorporated a number of different specializations. One avenue has been data-structure aware prefetching, where regular memory accesses guide irregular access prefetches. The system is specialized to know which data structures are regularly and irregularly accessed, and can perform the prefetching accordingly. Other approaches have been accelerator-oriented, creating specialized graph analytics accelerators that strive for energy efficiency. These approaches have involved specialized pipelines, such as separate modules for node and edge processing, processing near-memory, and on-chip scratchpads. Lastly, other prior work has focused on memory subsystem customizations, including reserving caches for nodes that are expected to be accessed the most frequently. All of these hardware-oriented approaches impose significant application restrictions, such as requiring the vertex programming model, or require invasive architectural modifications. We need a less specialized, more general-purpose solution that is adaptable and easy to incorporate into modern heterogeneous, parallel systems.

## Slide 45: Prior Work on Graph Processing
Software-oriented techniques:
  Aim for scalable parallel solutions
    Thread-level-parallelism to exploit MLP
    Complex scheduling routines
    Dynamic adjustments based on runtime characteristics
Well-known frameworks
  GraphMat [Sundaram PVLDB ’15]
  Gunrock [Wang PPoPP ’16]
  GraphIt [Zhang PACMPL ‘18]
Limited by the hardware resources, need flexible backend target
Software-based approaches focus on algorithmic improvements rather than targeting the LLAMAs with hardware innovations
Notes: Prior work has extensively explored improving graph processing from both ends of the computing stack.
Software-based techniques in general provide frameworks that aim to be scalable, parallel solutions on shared memory systems. These works use thread-level-parallelism to address memory latency bottlenecks. By having multiple threads issue irregular memory accesses simultaneously, these techniques can exploit Memory Level Parallelism (MLP). Additionally, these techniques often involve complex scheduling routines and dynamic adjustments based on runtime characteristics. While these approaches are effective for performance improvements, they are limited by the underlying hardware, for example the number of threads or cores available. Thus, we need a flexible hardware solution that synergizes with the efforts of these approaches, such as a flexible backend target that exposes the long-latency memory access bottlenecks.
Meanwhile, hardware-based approaches have incorporated a number of different specializations. One avenue has been data-structure aware prefetching, where regular memory accesses guide irregular access prefetches. The system is specialized to know which data structures are regularly and irregularly accessed, and can perform the prefetching accordingly. Other approaches have been accelerator-oriented, creating specialized graph analytics accelerators that strive for energy efficiency. These approaches have involved specialized pipelines, such as separate modules for node and edge processing, processing near-memory, and on-chip scratchpads. Lastly, other prior work has focused on memory subsystem customizations, including reserving caches for nodes that are expected to be accessed the most frequently. All of these hardware-oriented approaches impose significant application restrictions, such as requiring the vertex programming model, or require invasive architectural modifications. We need a less specialized, more general-purpose solution that is adaptable and easy to incorporate into modern heterogeneous, parallel systems.

## Slide 46: Prior Work on Latency Tolerance
Decoupling techniques
  Decoupled Access/Execute [Smith ISCA ‘82]
  Decoupled Supply/Compute [Ham MICRO ‘15]
Automatic parallelization
  DSWP [Rangan PACT ‘04]
  Automatic decoupled thread extraction [Ottoni MICRO ‘05]
Helper threads
  Pre-execution threads [Luk ISCA ‘01]
  Automatic pre-execution thread execution [Kim ASPLOS ‘02]
Loss of decoupling with control flow dependencies in graph applications
Inaccurate prefetching and additional threads incur energy overhead
Work balance heuristic does not account for latency variability due to memory hierarchy
Notes: Prior work has extensively explored improving graph processing from both ends of the computing stack.
Software-based techniques in general provide frameworks that aim to be scalable, parallel solutions on shared memory systems. These works use thread-level-parallelism to address memory latency bottlenecks. By having multiple threads issue irregular memory accesses simultaneously, these techniques can exploit Memory Level Parallelism (MLP). Additionally, these techniques often involve complex scheduling routines and dynamic adjustments based on runtime characteristics. While these approaches are effective for performance improvements, they are limited by the underlying hardware, for example the number of threads or cores available. Thus, we need a flexible hardware solution that synergizes with the efforts of these approaches, such as a flexible backend target that exposes the long-latency memory access bottlenecks.
Meanwhile, hardware-based approaches have incorporated a number of different specializations. One avenue has been data-structure aware prefetching, where regular memory accesses guide irregular access prefetches. The system is specialized to know which data structures are regularly and irregularly accessed, and can perform the prefetching accordingly. Other approaches have been accelerator-oriented, creating specialized graph analytics accelerators that strive for energy efficiency. These approaches have involved specialized pipelines, such as separate modules for node and edge processing, processing near-memory, and on-chip scratchpads. Lastly, other prior work has focused on memory subsystem customizations, including reserving caches for nodes that are expected to be accessed the most frequently. All of these hardware-oriented approaches impose significant application restrictions, such as requiring the vertex programming model, or require invasive architectural modifications. We need a less specialized, more general-purpose solution that is adaptable and easy to incorporate into modern heterogeneous, parallel systems.

## Slide 47: Decoupling Techniques
DAE [Smith ISCA ‘82]: static division of a program into two independent instruction streams or “compiler slices”
  Access thread
    Handles memory access and address computation; ”produces” data
  Execute thread
    Performs computation; “consumes” data
DeSC [Ham MICRO ‘15] maps Access/Execute threads to Supply/Compute cores
2015
1982
DAE: Decoupled Access/Execute
DeSC: Decoupled Supply/Compute
par for (v : worklist)
node_dist = dist[v]
for (n, e_val : neighbors[v])
new_dist = node_dist + e_val
updated = RMW_MIN(&dist[n], new_dist)
if (updated)
wl_idx = RMW_ADD(&idx, 1)
new_worklist[wl_idx] = n
Parallel Push-Based SSSP Kernel
Supply
Compute
Value Computation
Shared L2 Cache
Address Calculation
St. Value Buffer
St. Address Buffer
Comm. Queue
L1 Cache
L1 Cache
Main Memory
Term. Ld. Buffer
Supply slice
Compute slice
Notes: The Decoupled Access/Execute or DAE paradigm was first proposed decades ago by James E. Smith to address processor/memory communication latency. This technique statically divides a program into two independent instruction streams: the Access and Execute threads. This division process is also known as slicing, which is an established compiler technique. The Access thread is responsible for memory address computation and accesses to the memory hierarchy and the Execute thread performs computation.
The Decoupled Supply/Compute or DeSC technique was more recently proposed to improve upon DAE with the addition of out-of-order communication. In DeSC, the Access and Execute threads become data supply and computation cores, also known as the Supply and the Compute. Essentially, the Supply “produces” data for the Compute to “consume”.
In the diagram on the right, the compiler statically slices the SSSP kernel into Supply and Compute source code slices, and these slices are mapped onto two separate processors that operate concurrently. They communicate by the Supply producing data and placing it on a queue for the Compute to consume. Stores are decoupled since the Supply performs address computation and the Compute usually determines values to store. The store address buffer therefore maintains addresses of values that have yet to be determined while the store value buffer holds values that might need to be forwarded to later loads. I will go into further details about the terminal load buffer later.
As you can see in the image on the right, all loads in the original source code are performed on the Supply. The Supply sends the requests to memory and effectively produces the data that is loaded. The Compute then consumes this loaded data.
For all stores in the original source code, the address is determined on the Supply and the value is determined by the Compute. The Supply receives the value from the Compute and is then responsible for sending the store request to the memory hierarchy. All arithmetic computation is done on the Compute.

## Slide 48: Decoupling Techniques
DAE [Smith ISCA ‘82]: static division of a program into two independent instruction streams or “compiler slices”
  Access thread
    Handles memory access and address computation; ”produces” data
  Execute thread
    Performs computation; “consumes” data
DeSC [Ham MICRO ‘15] maps Access/Execute threads to Supply/Compute cores
2015
1982
DAE: Decoupled Access/Execute
DeSC: Decoupled Supply/Compute
par for (v : worklist)
node_dist = dist[v]
for (n, e_val : neighbors[v])
new_dist = node_dist + e_val
updated = RMW_MIN(&dist[n], new_dist)
if (updated)
wl_idx = RMW_ADD(&idx, 1)
new_worklist[wl_idx] = n
Parallel Push-Based SSSP Kernel
par for (v : worklist)
node_dist = LOAD(&dist[v])
PRODUCE(node_dist)
for (n, e_val : neighbors[v])
new_dist = CONSUME()
updated = RMW_MIN(&dist[n], new_dist)
PRODUCE(updated)
if (updated)
wl_idx = RMW_ADD(&idx, 1)
STORE_ADDR(&new_worklist[wl_idx])
par for (v : worklist)
node_dist = CONSUME()
for (n, e_val : neighbors[v])
new_dist = node_dist + e_val
PRODUCE(new_dist)
updated = CONSUME()
if (updated)
STORE_VAL(n)
Supply
Compute
Notes: On the right is an example of the compiler slicing performed.
All loads in the original source code are performed on the Supply. The Supply sends the requests to memory and effectively produces the data that is loaded. The Compute then consumes this loaded data.
For all stores in the original source code, the address is determined on the Supply and the value is determined by the Compute. The Supply receives the value from the Compute and is then responsible for sending the store request to the memory hierarchy. All arithmetic computation is done on the Compute.

## Slide 49: Exploiting Terminal Loads
Applications can involve long-latency loads
  The Supply has to stall waiting for their data to return from memory
  In decoupled setting, the consumer of this data is often mapped onto the Compute
Terminal loads: loads that have no dependencies on the Supply
  The Supply does not occupy pipeline resources waiting for their requests
  These loads can complete early and be maintained separately from other loads
  Terminal loads help maintain longer Supply runahead and exploit MLP
idx = 0
par for (r : sparse_rows)
for (c : sparse_cols[r])
sparse_val = sparse[idx]
idx++
ptr = r*NUM_ROWS + c
dense_val = dense[ptr]
prod = sparse_val * dense_val
result[idx] = prod
SDHP Kernel
idx = 0
par for (r : sparse_rows)
for (c : sparse_cols[r])
sparse_val = LOAD(&sparse[idx])
PRODUCE(sparse_val)
idx++
ptr = r*NUM_ROWS + c
dense_val = LOAD(&dense[ptr])
PRODUCE(dense_val)
STORE_ADDR(&result[idx])
idx = 0
par for (r : sparse_rows)
for (c : sparse_cols[r])
sparse_val = CONSUME()
idx++
ptr = r*NUM_ROWS + c
dense_val = CONSUME()
prod = sparse_val * dense_val
STORE_VAL(prod)
Supply
Compute
Terminal loads, no memory dependencies
Only used on the Compute
Values used in Compute operation
Notes: Naturally, many applications have data dependencies and stalling the Supply inhibits it from exploiting MLP. Furthermore, the Compute can catch up and have to wait for data from the Supply, incurring the cost of memory access latency. However, in decoupled architectures, the consumer of loads is often mapped onto the Compute, so DeSC exploits when this occurs.
One of the key innovations of DeSC was the concept of terminal loads, loads that have no data dependencies on the Supply. These loads allow the Supply to not occupy pipeline resources when it is waiting for the memory system to service requests because the returned data is no longer needed on the Supply. It can therefore issue new memory requests before the data returns from previous requests.
Therefore, many terminal loads can commit early and be enqueued in a specialized buffer called the Terminal Load Buffer. Their data is then enqueued based on when they are needed in program order. This prevents the Compute from waiting on data from memory and maintains longer Supply runahead distances. And with multiple accesses issued early in succession, memory-level parallelism or MLP is exploited.
If we can exploit MLP, then we can mitigate the memory latency bottlenecks of LLAMAs!

## Slide 50: Decoupling Hardware Support
Value Computation
Shared L2 Cache
Address Calculation
St. Value Buffer
St. Address Buffer
Comm. Queue
Term. Load Buffer
Supply
Compute
L1 Cache
L1 Cache
Main Memory
Blue arrows indicate datapath for terminal loads.
Communication Queue
  Holds data from loads the Supply has completed
Store Address Buffer
  Holds addresses of STORE_ADDR instructions whose values have yet to be calculated
Store Value Buffer
  Holds computed values to be forwarded to dependent loads
Terminal Load Buffer
  Holds terminal load data

## Slide 51: GraphAttack! Tolerates Latency in Graph Applications by Making NMAs Asynchronous
time
LD(dist)
InO Core
if
RMW_ADD
ST(n)
(a) In-Order Execution
add
if
RMW_ADD
ST(n)
add
if
RMW_ADD
ST(n)
add
par for (v : worklist)
node_dist = LOAD(&dist[v])
for (n, e_val : neighbors[v])
new_dist = node_dist + e_val
updated = RMW_MIN(&dist[n], new_dist)
if (updated)
wl_idx = RMW_ADD(&idx, 1)
STORE(&new_worklist[wl_idx], n)
Original Push-Based Parallel SSSP Kernel
RMW_MIN
RMW_MIN
RMW_MIN
= NMA (long-latency)
Due to dependencies, each instruction must wait for the previous one to complete.
Notes: To illustrate how FAST-LLAMAs mitigates latency effects in graph applications, we compare three different instruction execution timelines of the parallelized SSSP kernel. The first is the original code execution with no decoupling, the second is a traditional DAE-based approach approach, and the third is FAST-LLAMAs. In all timelines, the LLAMAs are highlighted with dotted blue boxes.
The first execution timeline corresponds to the original source code seen on the bottom right. Since this code is operating on an in-order core, we see that every instruction starts after its previous instruction completes and there is no overlapping of instructions. There is additional stalling waiting for the LLAMAs to complete, as these often have to retrieve data from DRAM.
We then focus on using a DAE-based approach. In the second execution timeline, we see that all memory operations are executed by the Supply, including the LLAMA. DAE does not support RMWs, but the entire RMW is optimistically mapped onto the Supply in this case to avoid extra communication costs between the Supply and the Compute. However, there is still a control flow dependence and the Supply has to wait for it to be resolved before it can perform worklist updates. Thus, this approach doesn’t mitigate the long-latency effects of the LLAMA since the Supply does not run ahead of the Compute.
In the third and final execution timeline corresponding to the FAST-LLAMAs decoupled source code, we see that there is no longer a control flow dependence on the Supply. This allows the Supply to run ahead of the Compute and issue multiple LLAMA memory requests. As seen by the overlapping of the LLAMAs, MLP is exploited. Meanwhile, the Compute handles computation and never has to wait on the Supply aside from an initial warm-up period.

## Slide 52: GraphAttack! Tolerates Latency in Graph Applications by Making NMAs Asynchronous
time
Supply
Compute
(b) DeSC
LD(dist)
if
RMW_ADD
ST_ADDR(n)
add
if
RMW_ADD
ST_ADDR(n)
add
if
RMW_ADD
ST_ADDR(n)
add
RMW_MIN
RMW_MIN
RMW_MIN
if
if
if
SV(n)
SV(n)
SV(n)
Parallel Push-Based SSSP Kernel Supply Slice
par for (v : worklist)
node_dist = LOAD(&dist[v])
PRODUCE(node_dist)
for (n, e_val : neighbors[v])
new_dist = CONSUME()
updated = RMW_MIN(&dist[n], new_dist)
PRODUCE(updated)
if (updated)
wl_idx = RMW_ADD(&idx, 1)
STORE_ADDR(&new_worklist[wl_idx])
par for (v : worklist)
node_dist = CONSUME()
for (n, e_val : neighbors[v])
new_dist = node_dist + e_val
PRODUCE(new_dist)
updated = CONSUME()
if (updated)
STORE_VAL(n)
Parallel Push-Based SSSP Kernel Compute Slice
= NMA (long-latency)
Control flow dependence on the NMA causes Supply to stall!
Notes: To illustrate how FAST-LLAMAs mitigates latency effects in graph applications, we compare three different instruction execution timelines of the parallelized SSSP kernel. The first is the original code execution with no decoupling, the second is a traditional DAE-based approach approach, and the third is FAST-LLAMAs. In all timelines, the LLAMAs are highlighted with dotted blue boxes.
The first execution timeline corresponds to the original source code seen on the bottom right. Since this code is operating on an in-order core, we see that every instruction starts after its previous instruction completes and there is no overlapping of instructions. There is additional stalling waiting for the LLAMAs to complete, as these often have to retrieve data from DRAM.
We then focus on using a DAE-based approach. In the second execution timeline, we see that all memory operations are executed by the Supply, including the LLAMA. DAE does not support RMWs, but the entire RMW is optimistically mapped onto the Supply in this case to avoid extra communication costs between the Supply and the Compute. However, there is still a control flow dependence and the Supply has to wait for it to be resolved before it can perform worklist updates. Thus, this approach doesn’t mitigate the long-latency effects of the LLAMA since the Supply does not run ahead of the Compute.
In the third and final execution timeline corresponding to the FAST-LLAMAs decoupled source code, we see that there is no longer a control flow dependence on the Supply. This allows the Supply to run ahead of the Compute and issue multiple LLAMA memory requests. As seen by the overlapping of the LLAMAs, MLP is exploited. Meanwhile, the Compute handles computation and never has to wait on the Supply aside from an initial warm-up period.

## Slide 53: GraphAttack! Tolerates Latency in Graph Applications by Making NMAs Asynchronous
Terminal RMWs operate asynchronously, overlapped with later instructions
Parallel Push-Based SSSP Kernel Producer Slice
par for (v : worklist)
node_dist = LOAD(&dist[v])
new_dist = node_dist + e_val
for (n, e_val : neighbors[v])
RMW_MIN_ISSUE(&dist[n], new_dist)
// RMW_MIN_ISSUE produces “updated”
par for (v : worklist)
for (n, e_val : neighbors[v])
updated = CONSUME()
if (updated)
wl_idx = RMW_ADD(&idx, 1)
STORE(&new_worklist[wl_idx])
Parallel Push-Based SSSP Kernel Consumer Slice
= NMA (long-latency)
No Producer dependencies on the NMA!
Begin next loop iteration
time
Producer
Consumer
(c) GraphAttack!
LD(dist)
if
RMW_ADD
ST(n)
add
add
add
RMW issue
RMW issue
RMW issue
if
RMW_ADD
ST(n)
if
RMW_ADD
ST(n)
RMW_MIN
RMW_MIN
RMW_MIN
AAB
Consumer does not have to wait
Producer has no dependencies on the NMA, runs ahead and begins next loop iteration
Notes: To illustrate how FAST-LLAMAs mitigates latency effects in graph applications, we compare three different instruction execution timelines of the parallelized SSSP kernel. The first is the original code execution with no decoupling, the second is a traditional DAE-based approach approach, and the third is FAST-LLAMAs. In all timelines, the LLAMAs are highlighted with dotted blue boxes.
The first execution timeline corresponds to the original source code seen on the bottom right. Since this code is operating on an in-order core, we see that every instruction starts after its previous instruction completes and there is no overlapping of instructions. There is additional stalling waiting for the LLAMAs to complete, as these often have to retrieve data from DRAM.
We then focus on using a DAE-based approach. In the second execution timeline, we see that all memory operations are executed by the Supply, including the LLAMA. DAE does not support RMWs, but the entire RMW is optimistically mapped onto the Supply in this case to avoid extra communication costs between the Supply and the Compute. However, there is still a control flow dependence and the Supply has to wait for it to be resolved before it can perform worklist updates. Thus, this approach doesn’t mitigate the long-latency effects of the LLAMA since the Supply does not run ahead of the Compute.
In the third and final execution timeline corresponding to the FAST-LLAMAs decoupled source code, we see that there is no longer a control flow dependence on the Supply. This allows the Supply to run ahead of the Compute and issue multiple LLAMA memory requests. As seen by the overlapping of the LLAMAs, MLP is exploited. Meanwhile, the Compute handles computation and never has to wait on the Supply aside from an initial warm-up period.

## Slide 54: Prior Work
Desired Features:
  Programmability
  Portability
  High Hardware Utilization
  Adoptability: Can be easily integrated into existing Hardware systems.
Notes:   This is a Table from the ISCA’21 submission of OpenLT. I have detailed some of the approaches in this table already,, but here there is some more extent literature
  The table describes features of each technique that makes it adoptable practice, on a SoC design:
  The table checks:
  -whether the approach requires Core modifications.
  -whether it is software portable or its compilation uses ISA-specific instructions,
  -whether it is also performant on an area-efficient cores with small instruction windows.
The last column of the table checks if the approach Leverages program knowledge.
Extracting program information saves area in the often-large structures used in predictors.
OpenLT is the first work the achieve all these features, requiring no core modifications, it is performant and area-efficient approach!

## Slide 55: References in Table I
  [4] Graph Prefetching [Ainsworth ICS’16]
  [6] Programmable, event-triggered [Ainsworth ASPLOS ‘18]
  [12] DROPLET [Basak HPCA ‘19]
  [17] Outrider [Crago ISCA ‘11]
  [22] PIPE decoupled architecture [Goodman SIGARCH ‘85]
  [23] Decoupled Supply/Compute [Ham MICRO ‘15]
  [35] Software Controlled Pre-execution [Luk ‘ISCA 01]
  [36] ZS-1 [Mangione-Smith HICSS’90]
  [40] Pipette [Nguyen MICRO ‘20]
  [41] Triggering Instructions [Parashar ISCA’13]
  [43] DSWP [Rangan PACT’04]
  [46] Decoupled Access-Execute [Smith ISCA’82]
  [47] Slipstream Processors [Sundaramoorthy ASPLOS ‘00]
  [50] MT-DCAE [Sung SIGARCH’01]
  [52] Clairvoyance [Tran CGO’17]
  [53] SWOOP [Tran PLDI’18]
  [57] Indirect Memory Prefetcher [Yu MICRO’15]
Notes: And These are the references shown in the previous Table

## Slide 56: GraphAttack! Tolerates Latency in Graph Applications by Making NMAs Asynchronous
time
LD(dist)
InO Core
if
RMW_ADD
ST(n)
(a) In-Order Execution
(b) DeSC
add
par for (v : worklist)
node_dist = LOAD(&dist[v])
for (n, e_val : neighbors[v])
new_dist = node_dist + e_val
updated = RMW_MIN(&dist[n], new_dist)
if (updated)
wl_idx = RMW_ADD(&idx, 1)
STORE(&new_worklist[idx], n)
if
RMW_ADD
ST(n)
add
if
RMW_ADD
ST(n)
add
Original Push-Based Parallel SSSP Kernel
RMW_MIN
RMW_MIN
RMW_MIN
GraphAttack! eliminates NMA dependencies, so decoupling achieves latency tolerance on graph applications!
time
Supply
Compute
LD(dist)
if
RMW_ADD
ST_ADDR(n)
add
if
RMW_ADD
ST_ADDR(n)
add
if
RMW_ADD
ST_ADDR(n)
add
RMW_MIN
RMW_MIN
RMW_MIN
if
if
if
SV(n)
SV(n)
SV(n)
time
Producer
Consumer
(c) GraphAttack!
LD(dist)
if
RMW_ADD
ST(n)
add
add
add
RMW issue
RMW issue
RMW issue
if
RMW_ADD
ST(n)
if
RMW_ADD
ST(n)
RMW_MIN
RMW_MIN
RMW_MIN
AAB
Notes: To illustrate how FAST-LLAMAs mitigates latency effects in graph applications, we compare three different instruction execution timelines of the parallelized SSSP kernel. The first is the original code execution with no decoupling, the second is a traditional DAE-based approach approach, and the third is FAST-LLAMAs. In all timelines, the LLAMAs are highlighted with dotted blue boxes.
The first execution timeline corresponds to the original source code seen on the bottom right. Since this code is operating on an in-order core, we see that every instruction starts after its previous instruction completes and there is no overlapping of instructions. There is additional stalling waiting for the LLAMAs to complete, as these often have to retrieve data from DRAM.
We then focus on using a DAE-based approach. In the second execution timeline, we see that all memory operations are executed by the Supply, including the LLAMA. DAE does not support RMWs, but the entire RMW is optimistically mapped onto the Supply in this case to avoid extra communication costs between the Supply and the Compute. However, there is still a control flow dependence and the Supply has to wait for it to be resolved before it can perform worklist updates. Thus, this approach doesn’t mitigate the long-latency effects of the LLAMA since the Supply does not run ahead of the Compute.
In the third and final execution timeline corresponding to the FAST-LLAMAs decoupled source code, we see that there is no longer a control flow dependence on the Supply. This allows the Supply to run ahead of the Compute and issue multiple LLAMA memory requests. As seen by the overlapping of the LLAMAs, MLP is exploited. Meanwhile, the Compute handles computation and never has to wait on the Supply aside from an initial warm-up period.

## Slide 57: Further Comparison of Latency Tolerance Techniques for Irregular Accesses
Technique | Latency Tolerance | Energy Efficiency | Scalability | Memory Traffic | Core Model Flexibility | Memory Subsystem Flexibility
DSWP [Ottoni MICRO ‘05] | Cyclical dependencies inhibit proper load balancing and LLAMA latency tolerance | Poor energy efficiency due to lack of latency tolerance | Communication latencies inhibit scalability | No additional memory traffic | Agnostic to core model | No modifications to memory hierarchy
Event-Triggered Prefetcher [Ainsworth ASPLOS ‘18] | Can tolerate LLAMA latency only for accurately prefetched LLAMAs (about 80%) | Additional energy of prefetching units (and hardware support) + DRAM energy due to inaccurate prefetches | Limited, bandwidth saturated faster with prefetching | Additional traffic due to inaccurate prefetches | Relies on OoO cores for greater ILP and MLP | Need to support snooping of data brought into L1, store data structure tag in MSHR
DROPLET [Basak HPCA ‘19] | Can tolerate LLAMA latency only for accurately prefetched LLAMAs (about 70%) | Additional energy of data-aware streamer and memory controller based prefetcher + DRAM energy due to inaccurate prefetches | Limited, bandwidth saturated faster with prefetching | Additional traffic due to inaccurate prefetches | Relies on OoO cores for greater ILP and MLP | Need to support data-aware L2 streamer, memory controller based prefetcher, extra bits to track irregularly accessed data
GraphAttack! | Tolerates all LLAMA latencies (excluding warm-up period) | In-order cores achieve greater energy efficiency over OoO | Superlinear scaling with respect to number of cores | No additional memory traffic | Agnostic to core model | No modifications to memory hierarchy
Notes: .

## Slide 58: GraphAttack! Limitations
Dynamically go through linked list of neighbors
Does not guarantee latency tolerance for arbitrary programs
  Linked-lists, recursion, and other self-dependencies pose challenges
  Competitive implementations utilize 1D, linear data structures
Designed for efficient data supply
  Imposes heavy resource utilization for compute-bound workloads
  Focuses on emerging workloads that modern technology trends struggle with
Bandwidth saturation
  Orthogonal to bandwidth efficiency techniques, e.g. graph-specialized caching
while (neighbor != NULL)
edge_val = neighbor -> val
...
neighbor = neighbor -> next
Linked List Example
Compiler
ERROR: Cannot decouple program because the dependence graph is cyclic!
New NMA
Cyclical dependences
Control flow dependence on NMA
Notes: Is example necessary?